## Slide 1
Bacterial endospores: structure, resistance and sporicidal testing
Jean-Yves Maillard
Cardiff School of Pharmacy and Pharmaceutical Sciences
Cardiff University

## Slide 2
Endospores & susceptibility to biocides
Tests for sporicidal activity
Impact of targeting endospores on formulation design
Sporicides and surface applications
OVERVIEW
1
J-Y Maillard – WFHSS Lille 2015

## Slide 3
ENDOSPORES AND SUSCEPTIBILITY TO BIOCIDES
2
J-Y Maillard – WFHSS Lille 2015

## Slide 4
ENDOSPORES & SUSCEPTIBILITY TO BIOCIDES
prions
bacterial spores
protozoal cysts
mycobacteria
naked viruses
vegetative Gram-negative
fungi
protozoa
vegetative Gram-positive
enveloped viruses
Low
Level of susceptibility
High
SPORICIDES
3
HLD
J-Y Maillard – WFHSS Lille 2015
STERILISATION

## Slide 5
SPORE CORE
SPORE COATS
EXOSPORIUM
CORTEX
INNER MEMBRANE
Barrier to biocides
Degradation ?
Persistence on surfaces
Small Acid Soluble Proteins (SASPs)
Protection of nucleic acid
Low water content
Protection of proteins
Barrier to biocides
Physical pressure to inner membrane
Highly compressed
Barrier to biocide
Barrier to rehydration
Leggett et al. J Appl Microbiol 2012; 113: 485-98.
4
ENDOSPORES & SUSCEPTIBILITY TO BIOCIDES
J-Y Maillard – WFHSS Lille 2015

## Slide 6
SPORE CORE
EXOSPORIUM
CORTEX
INNER MEMBRANE
Hypochlorites, chlorine dioxide, hydrogen peroxide, ozone, glutaraldehyde, ethylene oxide, iodine, chlorhexidine
Oxidising agents
Hydrogen peroxide
Alkali, hypochlorites, chlorine dioxide,ozone, glutaraldehyde, iodine chlorhexidine
SPORE COATS
5
ENDOSPORES & SUSCEPTIBILITY TO BIOCIDES
J-Y Maillard – WFHSS Lille 2015

## Slide 7
SPORICIDAL ACTIVITY
Ethylene oxide
Glutaraldehyde
Formaldehyde
ortho-phthalaldehyde
Hydrogen peroxide
Peracetic acid
Chlorine dioxide
Ozone
“SPORISTATIC” ACTIVITY
Sodium hypochlorite
Sodium dichlororisocyanurate (?)
Chloramine-T
Calcium hypochlorite
Iodine and iodophors
Highly reactive compounds
High-level disinfection
Not formulations
Phenols and cresols
Quaternary ammonium compounds
Biguanides
Organic acids and esters
Alcohols
Russell AD. Clin Microbiol Rev 1990; 3:99-119.
6
ENDOSPORES & SUSCEPTIBILITY TO BIOCIDES
J-Y Maillard – WFHSS Lille 2015

## Slide 8
Maillard J-Y. J Hosp Infect 2011; 77:204-9.
Results difficult to compare - different methods
Examples of sporicidal activity of NaOCl and NADCC
Results from suspension tests are not necessarily the same as those from a carrier test
7
ENDOSPORES & SUSCEPTIBILITY TO BIOCIDES
J-Y Maillard – WFHSS Lille 2015

## Slide 9
BIOCIDES | COMPOSITION | TRANSMISSION
70% ethanol | Alcohol | High
HiBi Scrub | Chlorhexidine digluconate | High
Flash | Benzisothiazolinone | High
Steri-7 | Isothiazolin-benzalkonium chloride | High
Virusolve | Alkyl triamine/bromine | Low
Chlor-clean | Sodium dichloroisocyanurate | nill
Hydrogen peroxide vapour | Hydrogen peroxide vapour (400 ppm 1 min) | nill
Biocides efficacy against the transmission of C. difficile
Lawley et al. Appl Environ Microbiol 2010; 76: 6895-900
Murine model – disinfection of cages (15 mL for 10 min)
8
ENDOSPORES & SUSCEPTIBILITY TO BIOCIDES
J-Y Maillard – WFHSS Lille 2015

## Slide 10
TESTS FOR SPORICIDAL ACTIVITY
9
J-Y Maillard – WFHSS Lille 2015

## Slide 11
GERMINATION
SPORULATION
SPORICIDAL ACTIVITY
BACTERICIDAL
ACTIVITY
OUTGROWTH
10
SPORISTATIC ACTIVITY
TESTS FOR SPORICIDAL ACTIVITY
Principles
J-Y Maillard – WFHSS Lille 2015

## Slide 12
Sporicidal activity: Difference between the number of viable spores added to the test vessel and surviving spores following exposure… as measured following germination and outgrowth, and multiplication of vegetative bacteria (to form a visible colony)
Recovery and growth of vegetative bacteria
Germination
Outgrowth
Multiplication
(visible colony)
Spore suspension in buffer or dried on a surface
Addition of active
Neutralisation
11
TESTS FOR SPORICIDAL ACTIVITY
Principles
J-Y Maillard – WFHSS Lille 2015

## Slide 13
Dormant Spore
Neutralisation
Spore Treatment
Germinated Spore
Lysed Spore
No Growth
Sporicidal
No Growth
Sporicidal
Dormant Spore
No Growth
Sporicidal
Germination
Outgrowth
1.
2.
3.
6.
7.
5.
4.
12
TESTS FOR SPORICIDAL ACTIVITY
Principles
J-Y Maillard – WFHSS Lille 2015
Leggett et al. J Appl Microbiol, under review.

## Slide 14
Incomplete / No Neutralisation
Dormant Spore
Neutralisation
Spore Treatment
Dormant Spore
Partially Germinated Spore
Germinated Spore
Germinated Spore
No Growth
Bactericidal/Bacteristatic
Normal Growth
Sporistatic
Normal Growth
Sporistatic
Normal Growth
No activity
13.*
Germination
Outgrowth
9.
8.
10.
11.
12.
14.
15.
16.*
17.
18.
* Denotes the requirement for some additional agent (e.g. lysozyme) to resume germination
13
TESTS FOR SPORICIDAL ACTIVITY
Principles
J-Y Maillard – WFHSS Lille 2015
Leggett et al. J Appl Microbiol, under review.

## Slide 15
Comparison of standard test protocols on sporicidal efficacy
14
EN14347: Basic sporicidal activity
Temperature: 20ºC; contact time: 5 and 60 min; no soiling
EN13704: Sporicidal suspension test
Temperature: 20ºC; contact time: 5 and 60 min; no soiling
ASTM2197: Surface test – stainless steel disk
Temperature: 20ºC; contact time: 5 and 60 min; no soiling
AOAC 996.04: Surface test – porcelain carrier
Temperature: 20ºC; contact time: 5 and 60 min; no soiling
Aims: Comparative studies of efficacy test protocols
Bacillus subtilis: spore preparation according to EN14347 protocol
Clostridium difficile: spore preparation according to the Clospore protocol
TESTS FOR SPORICIDAL ACTIVITY
Effect of test methods on sporicidal activity
J-Y Maillard – WFHSS Lille 2015

## Slide 16
15
5 min contact time | Log10 Reduction (± SD) |  |  |  |  |  |  | 
BIOCIDES/PRODUCTS Clean condition | BS EN 14347 |  | BS EN 13704 |  | AOAC 966.04 |  | ASTM E2197 | 
 | C. diff | B. sub | C. diff | B. sub | C. diff | B. sub | C. diff | B. sub
Glutaraldehyde - 2% | 0.54 (0.26) | 1.92 (0.15) | 0.27 (0.20) | 0.00 (0.40) | -0.41 (0.08) | -0.09 (0.00) | 0.49 (0.04) | O.18 (0.03)
Ortho-phthalaldehyde- 0.55% | 1.73 (0.27) | 1.77 (0.05) | 0.65 (0.25) | -0.09 (0.34) | 1.76 (0.74) | 0.02 (0.00) | 1.66 (0.09) | -0.01 (0.02)
Ortho-phthalaldehyde- 0.65% | 1.19 (0.29) | 1.93 (0.32) | 0.73 (0.28) | -0.22 (0.37) | 2.35 (0.74) | 0.16 (0.00) | 1.77 (0.72) | 0.02 (0.04)
Didecyldimehtyl ammonium chloride -1% | 1.16 (0.35) | 1.87 (0.29) | 0.11 (0.11) | -0.24 (0.29) | 0.11 (0.15) | -0.04 (0.00) | 0.05 (0.13) | 0.13 (0.05)
Bis(aminopropyl)laurylamine – 1% | 0.99 (0.34) | 1.87 (0.23) | 0.22 (0.05) | 0.25 (0.57) | -0.10 (0.12) | -0.20 (0.00) | 1.15 (0.20) | 0.30 (0.02)
Amine -1% + quaternary ammonium- 1% | 1.05 (0.66) | 0.48 (0.09) | 0.15 (0.05) | 0.63 (0.15) | 0.40 (0.60) | -0.20 (0.00) | 0.06 (0.23) | 0.31 (0.05)
Anoxy-Twin-1200 ppm | >6.16 (0.25) | >6.81 (0.64) | >5.96 (0.17) | >4.88 (0.10) | 5.05 (0.08) | 3.65 (0.00) | >5.17 (0.77) | >5.31 (0.02)
Aniosept Activ – 2% | TBC | TBC | > 6.44 (0.03) | > 6.18 (0.07) | 5.05 (0.08) | 2.15 (0.00) | 2.12 (0.11) | 4.01 (0.16)
NaOCl 5000 ppm | >6.16 (0.25) | 1.36 (0.06) | >5.96 (0.17) | 1.36 (0.14) | 5.05 (0.08) | 0.95 (0.00) | >5.83 (0.00) | 0.38 (0.03)
TESTS FOR SPORICIDAL ACTIVITY
Effect of test methods on sporicidal activity
J-Y Maillard – WFHSS Lille 2015

## Slide 17
16
60 min contact time | Log10 Reduction (± SD) |  |  |  |  |  |  | 
BIOCIDES/PRODUCTS Clean condition | BS EN 14347 |  | BS EN 13704 |  | AOAC 966.04 |  | ASTM E2197 | 
 | C. diff | B. sub | C. diff | B. sub | C. diff | B. sub | C. diff | B. sub
Glutaraldehyde - 2% | 1.87 (0.50) | 0.56 (0.03) | 1.57 (0.12) | 0.44 (0.47) | 1.60 (0.22) | 0.12 (0.00) | 1.17 (0.08) | 0.66 (0.06)
Ortho-phthalaldehyde- 0.55% | >6.11 (0.33) | 0.62 (0.11) | >5.96 (0.17) | 0.48 (0.63) | 5.05 (0.08) | 0.19 (0.00) | 5.83 (0.02) | 0.29 (0.06)
Ortho-phthalaldehyde- 0.65% | >6.11 (0.33) | 0.56 (0.07) | >5.96 (0.17) | 0.77 (0.39) | 5.05 (0.08) | 0.12 (0.00) | >5.83 (0.00) | 0.20 (0.09)
Didecyldimehtyl ammonium chloride -1% | 2.31 (0.45) | 0.70 (0.16) | 0.23 (0.09) | 0.07 (0.72) | 0.44 (0.20) | 0.54 (0.00) | 0.39 (0.30) | 0.41 (0.05)
Bis(aminopropyl)laurylamine – 1% | 3.22 (0.55) | 0.69 (0.05) | 0.25 (0.09) | 0.60 (0.54) | -0.08 (0.17) | -0.07 (0.00) | 1.22 (020) | 0.40 (0.10)
Amine -1% + quaternary ammonium- 1% | 0.90 (0.20) | 1.02 (0.16) | 0.03 (0.03) | 0.68 (0.01) | 0.44 (0.04) | 0.11 (0.00) | 0.23 (0.17) | 0.48 (0.10)
Anoxy-Twin-1200 ppm | >6.11 (0.33) | >6.27 (0.00) | >5.96 (0.17) | >4.88 (0.10) | 5.05 (0.08) | >5.81 (0.00) | >5.83 (0.00) | >5.31 (0.02)
Aniosept Activ – 2% | 4.12 (0.60) | 3.54 (0.15) | >6.44 (0.03) | >6.18 (0.07) | 5.05 (0.08) | >5.81 (0.00) | >5.83 (0.00) | 5.06 (0.24)
NaOCl 5000 ppm | >6.11 (0.33) | >6.27 (0.00) | 5.96 (0.17) | >4.88 (0.10) | 5.05 (0.08) | >5.81 (0.00) | >5.83 (0.00) | 4.28 (0.07)
TESTS FOR SPORICIDAL ACTIVITY
Effect of test methods on sporicidal activity
J-Y Maillard – WFHSS Lille 2015
Notes: C. Difficile spores are more susceptible than B. subtilis spores
The test method affects the sporicidal activity results when a short contact time (5 min) is used.
Amine/QAC have no sporicidal activity
Chemical neutralisation of amines/QAC is an issue

## Slide 18
17
TESTS FOR SPORICIDAL ACTIVITY
Chemical neutralisation of amines/QAC
J-Y Maillard – WFHSS Lille 2015
 | Log10 Reduction (SD) |  |  |  |  |  |  |  | 
 | Didecyldimehtyl ammonium chloride |  |  | Bis(aminopropyl) laurylamine |  |  | Amine + quaternary ammonium |  | 
 | 0.5% | 1% | 2% | 0.5% | 1% | 2% | 0.5% | 1% | 2%
Neutralisation | 0.28 | 0.46 | 0.30 | 0.26 | 0.47 | 0.27 | 0.24 | 0.43 | 0.31
Filtration | 0.25 | 0.44 | 0.27 | 0.73 | 0.48 | 0.86 | 0.27 | 0.46 | 0.50

## Slide 19
18
TESTS FOR SPORICIDAL ACTIVITY
Chemical neutralisation of amines/QAC
J-Y Maillard – WFHSS Lille 2015
 | Filtration |  |  |  | Neutralisation |  |  | 
Dilution | Neat | -1 | -2 | -3 | Neat | -1 | -2 | -3
Didecyldimehtyl ammonium chloride |  |  |  |  |  |  |  | 
0.5% | >300 | >300 | >300 | >300 | 0 | 0 | >300 | 294
1% | >300 | >300 | >300 | >300 | 0 | 0 | 0 | >300
2% | >300 | >300 | >300 | 300 | 0 | 0 | 0 | 280
Bis(aminopropyl) laurylamine |  |  |  |  |  |  |  | 
0.5% | >300 | >300 | >300 | >300 | 0 | 0 | >300 | >300
1% | >300 | >300 | >300 | >300 | 0 | 0 | >300 | >300
2% | >300 | >300 | >300 | 101 | 0 | 0 | >300 | 298
Amine + quaternary ammonium |  |  |  |  |  |  |  | 
0.5% | >300 | >300 | >300 | 300 | 0 | 0 | >300 | >300
1% | >300 | >300 | >300 | >300 | 0 | 0 | >300 | >300
2% | >300 | >300 | >300 | 199 | 0 | 0 | 0 | 276

## Slide 20
IMPACT OF TARGETING ENDOSPORES ON FORMULATION DESIGN
19
J-Y Maillard – WFHSS Lille 2015

## Slide 21
FACTORS INHERENT TO THE BIOCIDE | 
Concentration | Concentration exponent (η)
Formulation | Including pH, surfactants, ion chelators etc.
 | Ingredients (compatibility)
Improving penetration
Spore coats/cortex – surfactants/wetting agents?
Triggering germination
Germinants – correct combination
Targeting cortex – enzymes?
Enhancing spore mechanical removal from surfaces
Exosporium? –surfactants/ wetting agents
Aggregates
20
ENDOSPORES AND FORMULATION DESIGN
Considerations about a product
J-Y Maillard – WFHSS Lille 2015

## Slide 22
21
B. subtilis strain name | Strain abbreviation | Strain description
B. subtilis PS533 | WT | Wild-type strain carrying plasmid pUB110, which contains a kanamycin resistance marker.
B. subtilis PS578 | α-β- | Two genes (sspA and sspB) that encode the two major α/β-type SASP were deleted
B. subtilis PS3394 | cotE- | Strain PS3394 carries pUB110 and contains a tetracycline resistance cassette inactivating the cotE gene essential for proper spore coat assembly.
FACTORS INHERENT TO THE BIOCIDE | 
Concentration | Concentration exponent (η)
Formulation | Including pH, surfactants, ion chelators etc.
 | Ingredients (compatibility)
ENDOSPORES AND FORMULATION DESIGN
Considerations about a product
J-Y Maillard – WFHSS Lille 2015

## Slide 23
22
Excipients altering the activity of XX (-%) against spores of B. subtilis PS3394(cotE-)
Log10 reduction in spores/mL relative to PAA only
aaa bbb ccc ddd eee fff ggg
Amphoteric Alkalinity Source Solvent Chelator
Surfactants
Excipients altering the activity of XX (-%) against spores of B. subtilis PS533 (WT)
Log10 reduction in spores/mL relative to PAA only
aaa bbb ccc ddd eee fff ggg hhh iii
Amphoteric surfactants Non-ionic surfactants Solvents
ENDOSPORES AND FORMULATION DESIGN
Considerations about a product
J-Y Maillard – WFHSS Lille 2015

## Slide 24
FACTORS INHERENT TO THE APPLICATION | 
Contact time | 
Temperature | Q10
Soiling | 
Relative humidity | Gaseous biocides, antimicrobial surfaces, wipes
Surface type | Permeability, nature etc.
Applicator | Delivery of the sporicide(s); wipe, spray, liquid
23
Applications:
Does my efficacy test reflect how the sporicide is delivered?
Compatibility of the materials/vessels/containers with the active
Effect of the applicator of target microorganisms (spores)
Require a realistic test protocol to enable the comparison of different formulation/applicator combinations
ENDOSPORES AND FORMULATION DESIGN
Considerations about a product
J-Y Maillard – WFHSS Lille 2015

## Slide 25
SPORICIDES & SURFACE APPLICATIONS
24
J-Y Maillard – WFHSS Lille 2015

## Slide 26
Possible scenarios for decontaminating high-touch environmental surfaces by wiping
Sattar & Maillard AJIC 2013;41:S97-S104.
25
SPORICIDES & SURFACE APPLICATIONS
J-Y Maillard – WFHSS Lille 2015

## Slide 27
ROLE OF WIPES – 3 STEP TEST (ASTM E2967-15 –May 2015)
Williams et al. J Hosp Infect 2007;67:329-35
Sattar et al. J Hops Infect 201, in press
Remove bioburden from a surface
Stage 1 – bacterial removal
How good are the wipes in removing microbial contaminants? (not killing effect)
Prevent transfer of bioburden from the wipe to other surfaces
Stage 2 – bacterial transfer “adpression tests”
Can the wipes transfer survivors to other surfaces (i.e. cross-contaminate)?
Where antimicrobial is present – kill the microbial bioburden
Stage 3 – Antimicrobial activity
Can the wipes kill the bacteria they remove?
26
SPORICIDES & SURFACE APPLICATIONS
J-Y Maillard – WFHSS Lille 2015

## Slide 28
Wipes | Bacterial Removal (log10 cfu/disk ± SD) 500 g surface pressure | Bacterial transfer following 10 s wiping time at 500 g surface pressure
Negative control | 1.13 (± 0.36) | 5 consecutive transfers. TNTC
NaOCl soaked wipe | 2.02 (± 0.21) | 5 consecutive transfers. TNTC
WIPE A | 4.09 (± 0.79) | No spore transferred
WIPE B | 0.22 (± 0.07) | 5 consecutive transfers. From 0 to TNTC
WIPE C | 1.30 (± 0.33) | 5 consecutive transfers. From 0 to TNTC
WIPE D | 0.57 (± 0.07) | 5 consecutive transfers. From 1 to TNTC
WIPE E | +0.08 (± 0.08) | 5 consecutive transfers. TNTC
WIPE F | 1.14 (± 0.65) | 5 consecutive transfers. From 83 to TNTC
WIPE G | 0.67 (± 0.11) | 5 consecutive transfers of ≤43 bacteria
WIPE H | 0.88 (± 0.13) | 5 consecutive transfers. From 2 to TNTC
WIPE J | 0.84 (± 0.66) | 5 consecutive transfers. From 40 to TNTC
USE OF WIPE BASED PRODUCTS – efficacy testing against C. difficile NCTC12727
Siani et al. AJIC 2011; 39(3), 212-218
SPORICIDES & SURFACE APPLICATIONS
27
J-Y Maillard – WFHSS Lille 2015

## Slide 29
APPROPRIATE TEST PROTOCOLS FOR DIFFERENT STAGES
Intelligent design (formulation)
Formulation/applicator combinations (can be used for product documentation)
Standard tests (product claim)
DELIVERY SYSTEM
FORMULATION
TARGET
MICROORGANISM
SURFACES
28
SPORICIDES & SURFACE APPLICATIONS
J-Y Maillard – WFHSS Lille 2015

## Slide 30
THANK YOU
29
J-Y Maillard – WFHSS Lille 2015